## Slide 1: Buzz Control
A short introduction
All used trademarks or trademark signs are the property of their respective owners.

## Slide 2: Goals
Control Microsoft Windows applications remotely without the need of mouse, keyboard and screen.
Full integration into Buzz 2 as well as other software applications, like Rebirth RB-338 or Generator.
Easy update of the controller.
Direct access to the audio I/O’s on the USB version of the controller (as separate Buzz 2 in/outputs or windows audio input/output devices).
Different sequencing options, like step sequencing, drum grid and analog sequencer.

## Slide 3: Controller overview
This is a layout picture of Buzz Control:

## Slide 4: Technical specifications
Case: 19” Rack case, 5 HE
LCD display: 128x64 pixels
Control elements: 48 knobs, 16 faders, 44 buttons, 1 alpha dial
Connectors: MIDI in, MIDI out, Serial I/O or USB I/O
Microcontrollers: 2x PIC 16c73a
Drivers: Windows 95/NT compatible DLL, VXD and DRV
Audio inputs: 16 stereo cinch inputs (USB version only)
Audio outputs: 2 stereo cinch outputs (USB version only)
Note: The controller itself is very simple because it only sends button, fader and knob data and receives LCD display data. The control elements aren’t interpreted by the controller directly. This has several advantages:
  The controller can be updated easily
  The microcontroller doesn’t need to be fast and there’s no need to place additional RAM onto the controller.
  The interface exists on the computer and can be accessed from developers by calling an API.
  Additional sequencing methods are available just by updating a driver and not by replacing hardware components

## Slide 5: USB vs. Serial Version
The USB version of the controller features additional audio in/ouputs.
Because the audio in/outputs are not statically linked to the faders, the user has many options how to link them. For example, the user can link mono inputs 1+2 (as a stereo input) to fader 1 to control the volume of both inputs as the same time, then put a 3 band EQ into Buzz 2 (which can be done with the controller) and assign the 3 knobs above fader 1 to hi, mid and low of the 3 band EQ. This would be a typical application for DJ’s. This gives the user the freedom he needs.
The serial version can be updated to the USB version just by replacing a single circuit board.

## Slide 6: User interface
The user interface is realized by the PC driver only, which means that the user interface can be adjusted when the users needs are changing.
The controller should be able to send out specified MIDI controllers when not connected to a computer, without displaying any data on the LCD display (due to the microcontrollers amount of RAM).
Flexible routing of all components (MIDI interface, audio I/O’s and control elements).

## Slide 7: Driver concepts
The driver on the Win95/NT platform handles all things like interpreting control element values, sequencing etc.
The driver sends the LCD display data back to the controller, so there’s no waste of RAM/ROM on the microcontroller, and therefore the microcontroller is very cheap.

## Slide 8: Implementation in Buzz 2
Full integration into Buzz 2, as well as full control of Buzz 2 by the controller only (useful for live performances).
Direct access to Buzz 2’s sequencer
Changing parameters of Buzz 2 while playing
Changing patterns on the fly while playing

## Slide 9: Implementation in other software applications
The implementation into other software applications need to be done by the manufacturers.
Buzz Control provides an API to let developers control the controller directly.
Audio I/O ports should be available as standard windows waveform I/O’s.